## Slide 1: Task 4.1: Pub/Sub MQTT System and Anomaly Detection
Ragini Gupta
University of Illinois-Urbana Champaign
(PI: Klara Nahrstedt)

## Slide 2: Task Goal
Design an end-to-end dataflow IoT platform using MQTT driven distributed streaming protocol for remote data monitoring, visualization and anomaly detection
Real-time sensor data streaming from MSA towers and application of unsupervised machine learning algorithms for anomaly detection to uncover hidden patterns and correlations, thus providing situational awareness.

## Slide 3
MQTT client application is employed to collect real-time IoT sensor data from MSA towers
Timeseries database (InfluxDB) is employed for sensor data ingestion & storage
Unsupervised machine learning algorithms and statistical methods are used to detect anomalous data points
Web-based real-time visualization platform is employed for data monitoring

## Slide 4
Designed for lightweight M2M communications
Application layer protocol, relies on underlying TCP
Can support upto 200k concurrent connections on a single broker
Message Queuing Telemetry Transport (MQTT)
HTTP | MQTT
Request-Response Paradigm | Publish-Subscribe Paradigm
Larger, few KBS | Small message size, header of 2 bytes
All messages get same service level | Three QoS settings
Data distribution: 1-to-1 | Data distribution: 1-to-1, 1-to-n, n-to-n
 | Low bandwidth usage, lower latency, higher network throughput, Utilization

## Slide 5
MQTT Protocol Sequence
Source: http://www.sharetechnote.com/html/IoT/App_Protocol_MQTT.html
Can use Wireshark Network Analysis tool for packet-level visualization
https://www.wireshark.org/docs/wsug_html_chunked/ChUseMainWindowSection.html

## Slide 6
Design Principle:
Utility Functions: CONNECT, SUBSCRIBE, UNSUBSCRIBE, PUBLISH, DISCONNECT
Topics: Form of addressing for clients to share information, hierarchal structure
“parent route/child route/..”
A topic is defined by a (Name, QoS) tuple where,
name: identifies topic within the domain
QoS: level of guarantee for delivery (supports: 0,1,2)
  Default QoS level set to 0, high frequency data
Maximum message size: 250 MB, Maximum Topic size: 65KB
For more information on MQTT packet structure and related specs, please refer:
http://docs.oasis-open.org/mqtt/mqtt/v3.1.1/os/mqtt-v3.1.1-os.html

## Slide 7
Connect to the live DVPG network via ethernet connection to the MSA router
MQTT- Explorer Client Application (Quick diagnostic test)
Paho MQTT Library (Python, Java) (For logging and collecting data)
Technical Approach

## Slide 8
Dataset Description:
Text files
String dictionary of dictionaries
Sensor Frequency 1Hz, 20 Hz (Sonic)
~ 20 GB/day

## Slide 9
Workflow
Technical Approach

## Slide 10
MQTT Pub-Sub Paradigm
Technical Approach
Publisher
Utility Functions:
CONNECT  Three parameters, Broker IP (Host), Port, KeepAlive (in seconds)
PUBLISH  Three Parameters,
Topic Name, Payload, QoS (by
default-0)

## Slide 11
Utility Functions:
On_Connect Callback: When broker responded to subscription request (CONNACK)
On_Message Callback: Called for each message received , msg is MQTTMessage class with members- topic, payload
Subscribe: Inside On_Connect(), subscription is renewed for each reconnection
Subscriber

## Slide 12
MQTT Message Payload and Decoding
Actual message payload  Binary buffer
To decode, need to know format in which Payload is sent:
  Text data: Decode using the UTF-8 decoder
  JSON formatted String: Decode as string+ deserialization of JSON string into dictionary
  File (binary data): No decoding
  Number: Typecast using int(msg.payload)

## Slide 13
Database and Visualization
Using Influxdb-Client Python Module
InfluxDB Database supports line protocol (to write points into database)
Transform data into line protocol text-based data format on-the-fly
  Three Key Parameters: Measurement (table name), Tags (Metadata), Fields (Values)
Write function to insert data into the bucket (database)
Parsing each Sensor data attribute and assigning attribute to tag/field/measurement within a JSON data structure

## Slide 14
Technical Approach
Grafana Dashboard
Ragini Gupta, et. al., "SVAD: End-to-end Sensory Data Analysis for IoBT-Driven Platforms", IEEE World Forum on Internet of Things (WF-IoT), 2021.
Grafana is an off-the-shelf software for creating charts, graphs, reports for dashboarding in real-time
Connects to InfluxDB database, FluxQL query language
Can create alert rules by defining thresholds on sensor values
Built-in alert services: Email, Discord, Slack, PagerDuty

## Slide 15
Anomalies: Irregularities in data that deviate from common statistical properties of a distribution including mean, median, modes, quartiles
Two significant features:
Occur very rarely in the data
Features differ from normal instances significantly
Applied techniques: Statistical method (Centroid based approach), Unsupervised ML (Isolation Forest, DBSCAN clustering)
Detecting anomalies/irregularities
Ragini Gupta, et. al., "SVAD: End-to-end Sensory Data Analysis for IoBT-Driven Platforms", IEEE World Forum on Internet of Things (WF-IoT), 2021.

## Slide 16
Approach
Algorithm:2 Using Centroid based approach for Anomalies | 
 | Input: R <- Data(humidity, temperature, pressure, solar irradiance, soil temp)
 | Output: Anomaly score of each point based on it’s distance from the centroid
 | Centroid (xc, yc, zc, wz, qz) = find_centroid(R), where xc = 1/n * , and so on.
 | Min-max normalization Transform i in R to i’ = (i-min)/ (max-min) where, max and min are maximum and minimum values in R
 | score <- Calculate anomaly score si for each point i’ in R based on centroid xc, yc, zc, wz, qz
 | return dictionary D, where Di is the timestamp, location, humidity, temperature.., soil temperature and anomaly score of the i-th point
Algorithm:2 Using Centroid based approach for Anomalies | 
 | Input: R <- Data(humidity, temperature, pressure, solar irradiance, soil temp)
 | Output: Anomaly score of each point based on it’s distance from the centroid
 | Min-max normalization Transform i in R to i’ = (i-min)/ (max-min) where, max and min are maximum and minimum values in R
 | score <- Calculate anomaly score si for each point i’ in R based on centroid xc, yc, zc, wz, qz
 | return dictionary D, where Di is the timestamp, location, humidity, temperature.., soil temperature and anomaly score of the i-th point

## Slide 17
    Methodology:
    Dataset
    Demonstrate time-stamps at which anomalies/outliers were found with their corresponding anomaly score (anomaly score: ranges from [0,1], 1 is most anomalous)
    Dimensions considered : Temp, Humidity, Barometric Pressure, Humidity, Solar Irradiance, Soil Temperature
    Anomaly Score: Distance of each point from the centroid
    Centroid based result format: [timestamp , dim-1, dim-2,dim-3,..,dim-n anomaly_score]
    Top 5 most anomalous points
    Timestamp, Anomaly Score
[timestamp, location(latitude/longitude), tower_number, Pressure, Temp, Humidity, Solar irradiance, Soil Temperature, Anomaly Score]
timestamp Anomaly Score

## Slide 18: Demo

## Slide 19
Steps: https://github.com/iobt/anomalyDetection_pubsub
Start your VM (password: virtualmachine1)
Open Pycharm Project >> mqtt_anomalyDetection
Start Moqsuitto broker on terminal window:
Start InfluxDB from terminal and open localhost:8086 on browser

## Slide 20
Create a new bucket on InfluxDB from http://localhost:8086
InfluxDB UI from browser

## Slide 21
Specify database name in Subscriber.py in python project
Run Subsriber.py and Publisher.py synchronously (run as independent processes)
  From cmd run:
  >> python3 /home/virtualmachine1/PycharmProjects/mqtt_anomalyDetection/Publisher.py
Optional: Start Grafana instance using:
>> sudo /bin/systemctl start grafana server
Execute Anomaly Detection.py from python project

## Slide 22
References:
https://github.com/iobt/anomalyDetection_pubsub
https://ieeexplore.ieee.org/document/9594944
On MQTT: http://docs.oasis-open.org/mqtt/mqtt/v3.1.1/os/mqtt-v3.1.1-os.html
On Influx QL Query (to query from Grafana query editor to InfluxDB): https://docs.influxdata.com/influxdb/v1.8/query_language/
Feel free to email for queries: raginig2@illinois.edu

## Slide 23
Three types of algorithms are exposed as anomaly detection services on the Weather-Sensor Data: Isolation Forest, DBSCAN clustering, Centroid based anomaly detection. Features (Temp, Humidity, Pressure)
    Anomalies: Data points that are extremely low, high, few or deviate significantly from normal data distribution
Anomaly Detection
Algorithm:1 Using Isolation Forest Algorithm for Anomalies | 
 | Input: R <- Data(humidity, temperature, pressure)
 | Output: Anomaly score of each point based on depth each point settles to and average path length
 | Let Q be the list of attributes in R
 | Randomly select an attribute q in Q
 | Randomly select a split point p from min and max values of attribute q in R
 | For each data point, i compute: Xl = i if i<p and Xr= i if i>p
 | score <- Calculate anomaly score s_i for each point i in Xl & Xr based on isolation forest approach
Algorithm:3 DBSCAN clustering | 
 | Input: R <- Data(humidity, temperature, pressure), eps – Minimum cluster distance, MinPts – Minimum points to form a cluster
 | Output: Cluster plot
 | Cluster index # C=1
 | For each unvisited point p in dataset R: Neighbors N = find the neighboring points of p # Find neighbors # mark p as visited
 | if N >= MinPts: N= N U N’
 | if p’ is not a member of any cluster:
 | Add p’ to cluster C